## Slide 1: Understanding Quantum Computing Abbas Omar University of Magdeburg

## Slide 2: Contents
Binary Computing
Logic Gates and Bit Representation
Dependent and Independent Bits
Matrix Representation of Logic Gates
Classical Harmonic Oscillator
Quantum Harmonic Oscillator and the Qubit
Superconducting Transmons as Qubits
Quantum Gates
Control and Readout of Qubits
Conclusions

## Slide 3: Binary Computing
Number Representations
  Decimal: 0,1,2,3,4,5,6,7,8,9 (10 Symbols)
  Hexadecimal: 0,1,2,3,4,5,6,7,8,9,A,B,C,D,E,F (16 Symbols)
  Octave: 0,1,2,3,4,5,6,7 (8 Symbols)
  Binary: 0,1 (2 Symbols)
Basic Operations: Addition and Multiplication
  Binary Multiplication: Addition + Shift Register

## Slide 4: Logic Gates and Shift Register
Logic Gates: AND, OR, XOR, NAND, NOR, XNOR, NOT
Shift Register

## Slide 5: Probabilistic Bit Representation

## Slide 6: Deterministic vs. Probabilistic
Deterministic is a special case of Probabilistic

## Slide 7: Dependent and Independent Bits
Independent Bits:
Example: Flipping two coins

## Slide 8: Dependent and Independent Bits
Combining Independent Bits:

## Slide 9: Bit Coupling
Independent (uncoupled) bits cannot offer:
Remember the term “Entanglement”

## Slide 10: Matrix Representation of Logic Gates
Combinational Logic Gates (No Feedback; No Memory)

## Slide 11: Combinational Logic
3-Bit Input

## Slide 12: Combinational Logic
General Features of Gate Matrices
  Deterministic
  Usually nonsquare
  Usually noninvertible (Irreversible Operations)
  Entries are 1’s and 0’s
  Each column has a single 1
  Deterministic inputs  Deterministic outputs
  Stochastic inputs  Stochastic outputs

## Slide 13: Sequential Logic and LFSR
Linear Feedback Shift Register (LFSR)
Example of dependent (coupled) bits
Function: Generating pseudorandom bit sequences
Randomness is limited (sequences are cyclic)

## Slide 14: Sequential Logic and LFSR
Gate state evolves in time, clock triggers the state change

## Slide 15: ATTENTION!
State Vector and Gate Matrix are defined differently for Sequential Logic

## Slide 16: Sequential Logic and LFSR
Cyclic States
States (pseudorandom bit sequences) depend on the initialization sequence b0
Maximum cycle length corresponds to generating all possible states except for the all-zero state

## Slide 17: Introducing Quantum Gates
Classical Combinational-Logic Gates
  Input and output variables are physically different (different wires)
  Their numbers are not necessarily equal
  Output changes simultaneously with input

## Slide 18: Introducing Quantum Gates
Attributes of Quantum Gates
  Single set of variables (qubits) for both input and output
  Quantum gates are just the time evolution of these variables
  Number of input and output variables is the same
  Gate matrix is square
  For a clock period Tc , the values at t=0 represent the input, and those at t=Tc represent the output
  Therefore, the gate operation is a temporal (evolution) process

## Slide 19: Introducing Quantum Gates
Attributes of Quantum Gates
  Direct and inverse gate operations are forward and reverse time evolutions
  Exchanging input and output variables corresponds to transposing the gate matrix
  Inverse matrix is therefore the conjugate transpose of the direct matrix
  Gate matrix is unitary

## Slide 20: Classical is a Special Case
Classical Gate Matrices
  Entries are 1’s and 0’s
  Each column is a unit vector (contains a single 1)
  Can always be made unitary (e.g. by adding dummy variables)
  Deterministic input  Deterministic output
Quantum Gate Matrices
  Unitary
  Deterministic input  Deterministic or Stochastic output
  Much higher Randomness as compared to classical sequential logic

## Slide 21: Converting Classical into Quantum
Classical XOR
Equivalent Quantum Gate CNOT (Controlled NOT)

## Slide 22: Converting Classical into Quantum
Equivalent Quantum Matrices
  Square
  Unitary  invertible
  Columns are all unit vectors (no repetition!)
  Number of different matrices is 2n! (n: number of Qbits)

## Slide 23: Classical Harmonic Oscillator
Known Examples
Characterized by a “Simple Harmonic Motion”

## Slide 24: Classical Harmonic Oscillator
Mass on a Spring

## Slide 25: Classical Quantum Oscillator
General Features

## Slide 26: Concept of Potential Well
The object (particle) is trapped within the potential well

## Slide 27: Quantum Harmonic Oscillator
All dynamic variables (position, momentum, etc.) become random processes (time-varying random variables)
Both position and momentum are continuous random variables
Energy is a discrete random variable
Only the corresponding probability distributions (real and positive) can be computed in terms of complex quantities known as Wave Functions
Wave Functions (defining the system States) are determined by, e.g., solving Schrödinger Equation

## Slide 28: Quantum Harmonic Oscillator

## Slide 29: Stationary Wave Functions (States)
Eigenfunctions of the time-independent Schrödinger Equation
Probability distributions are time-independent (Stationary)
Corresponding Eigenvalues En are the discrete random variable representing the total energy (Energy Quantization)

## Slide 30: Stationary States
Stationary Wave Functions are Energy Eigenstates

## Slide 31: Stationary States
The dynamic variables position and momentum are pure noise and don’t resemble time-varying signals
The quantized energies are Noise Energies and are proportional to the noise variance

## Slide 32: Coherent States
Linear Combination (Superposition) of the Stationary States

## Slide 33: Coherent States
Oscillating Probability Distribution

## Slide 34: Coherent States
Representation of the Probability Distributions of both Position and Momentum

## Slide 35: Coherent States
Contrary to thermal noise, quantum noise can interfere destructively in the coherent states

## Slide 36: Coherent States
Time Dependences of Position and Momentum are NOISY Signals
Position or Momentum

## Slide 37: Observation and Measurement
Quantum Mechanics postulates that any observation or measurement of the system destroys the time dependence (the signal part) of the probability distributions.
This must lead to a collapse to only one stationary state.
It is also postulated that the probability of collapsing to a certain stationary state after the observation or measurement is the square magnitude of its coefficient in the superposition describing the system prior to the observation or measurement.

## Slide 38: Observation and Measurement
Having been collapsed to a stationary state, the system energy becomes that of this state.
Destroying the signal part means dissipating its energy into heat (thermal noise).
Despite the fact that the energy measurement must result in a discrete random variable, the thermal noise resulted from dissipating the signal part converts it into a continuous one (something similar to the noise clouds surrounding a transmission constellation).

## Slide 39: L-C Circuit as Quantum Oscillator

## Slide 40: L-C Circuit as Quantum Oscillator
Either:
Or:

## Slide 41: Breaking the Harmonicity
Transmons: Replacing the linear inductor by a nonlinear superconducting Josephson Junction  Energy levels become differently spaced

## Slide 42: Superconducting Transmons
Only two states with the energy-level difference ω01
Other states become detuned
Two-State Wave Functions:

## Slide 43: Superconducting Transmons
Features

## Slide 44: Superconducting Transmons
Classically destroying “killing” the signal (the noiseless time varying part) through dissipation must result in changing the state to a stationary one (pure noise)
This is called Collapsing

## Slide 45: Bloch Sphere

## Slide 46: Bloch Sphere

## Slide 47: Bloch Sphere

## Slide 48: Transmons as a Qubits
Transmon State: Superposition of Two Energy Eigenstates
Corresponding Qubit:

## Slide 49: Analogy
Mach-Zehnder Interferometer

## Slide 50: Quantum Gates
Gate Matrices (unitary) can now have complex entries

## Slide 51: Quantum Gates
Unusual Gates (no classical counterparts)

## Slide 52: Qubit Control
Performing Gate Operations
Achieved by exciting the qubit by a resonant voltage or current source

## Slide 53: Qubit Control

## Slide 54: Qubit Control

## Slide 55: Qubit Control

## Slide 56: Qubit Readout

## Slide 57: Qubit Readout
Weak qubit-resonator coupling
Weak resonator-line coupling
Qubit and resonator are detuned
The weak energy exchange with the qubit fully
  destroys the signal part
Measuring the phase of the reflection coefficient

## Slide 58: Conclusions
A general overview on Quantum Computing has been given
Classical combinational and sequential gates have been compared
Quantum counterparts of combinational gates have been introduced and discussed
Transmon realization of a single qubit has been analyzed
Control and Readout of a single Transmon qubit have been presented